## Slide 1
SMART INDIA HACKATHON 2026
AnnaChain
A sensor box that travels with the food and proves what happened to it
Problem Statement ID - 26232
Problem Statement Title - Low-Cost IoT Blockchain Nodes for Farm-to-Fork Traceability
Theme - Agriculture, FoodTech & Rural Development
PS Category - Hardware
Organisation - Ministry of Food Processing Industries (MoFPI)
Team ID - ______________________
Team Name - ______________________
How It Works
SENSE
LOCK
SAVE
RE-SYNC
PROVE
Every reading is locked and saved on the device before it is ever sent.
When the signal returns, only the missing records are uploaded.
Why It Matters
₹140
per shipment. A throw-away logger costs ₹499.
350
records recovered after 29 hours with no signal.
3.8 yr
battery life, kept topped up by solar.
8
checks before any reading is trusted.
Store first, transmit second — so a stretch of road with no signal never becomes a hole in the cold-chain record.
Notes: Paste the official SIH 2026 logo in the clear space at the top right of every slide, from your Canva template. Upload as PDF only.

## Slide 2
Your Team
Name
ANNACHAIN — THE IDEA
@SIH Idea submission- Template
2
Our Solution - AnnaChain
AnnaChain is a low-cost, rugged, solar-powered sensor box that rides with the crate. It measures temperature, humidity and ethylene, locks every reading, and keeps working when the network is gone.
Three sensors in one box — temperature, humidity, ethylene
Tamper, movement and battery health as well
Secure chip signs each reading inside the device
Solar panel keeps the battery charged
Saves to flash first, sends afterwards
One shared gateway per truck over LoRa
Uploads only the records the server is missing
Proof written to a tamper-evident ledger
Stakeholder Impact
Farmers & FPOs
quality traced to the grower
Exporters
a record foreign buyers accept
Transporters
an alert while the truck can still be fixed
FSSAI / APEDA
recall only the affected pallets
Need for Solution
80% of India's cold chain is run by small operators who buy nothing today
81% of export rejections are paperwork, handling and temperature — not pesticides
10,000 reefer trucks exist against 62,000 needed
5-15% of fruit and vegetables lost after harvest
Uniqueness
Store first,
send second
a lost link cannot create a gap
Two-level
backup
node saves, gateway saves
Check before
you store
8 tests before a reading is believed
Nodes watch
each other
a faulty sensor is flagged, not called spoilage
High Level Overview
CRATE NODES
ESP32-S3 · sensors · secure chip
ONE GATEWAY
LoRa in · Wi-Fi / 4G out
SERVER
8 checks, then stored
LEDGER + AI
proof · shelf-life
Where It Runs
Farm gate and pack-house
Reefer truck and open truck
Cold store and mandi
Port, and the buyer's receiving dock
Notes: Do not read the panels. Point at Need for Solution, then at Uniqueness. Two panels, thirty seconds.

## Slide 3
Your Team
Name
TECHNICAL APPROACH
@SIH Idea submission- Template
3
End-to-End Flow — and What Happens With No Signal
ON THE CRATE
SWITCH ON
self-test · NFC links it to the shipment
SENSE every 5 min
temperature · humidity · ethylene
tamper · movement · battery
SIGN + ENCRYPT
secure chip, inside the device
SAVE ON THE DEVICE
flash, before any radio
IS THERE A SIGNAL?
SIGNAL?
NO SIGNAL
Keeps sensing and saving
Records 1001 … 1350 held in flash
Up to 90 days of storage
SIGNAL PRESENT
LoRa to the shared gateway
Gateway sends over MQTT/TLS
Wi-Fi, or 4G where there is none
when the signal returns, only the missing records go up
ON THE SERVER
8 CHECKS BEFORE ANYTHING IS STORED
✓
Is the device registered?
✓
Is the signature valid?
✓
Is the sequence correct?
✓
Is it a duplicate or replay?
✓
Is the timestamp sensible?
✓
Is the hash chain unbroken?
✓
Is the calibration still valid?
✓
Is the sensor healthy?
Analytics Engine
Q10 kinetics · rule-based classification
LEDGER
Fabric · GS1 EPCIS
DASHBOARD · ALERTS · REPORTS
WHAT ONE RECORD CARRIES
seq no
time
temp
humidity
ethylene
tamper
battery
signature
… plus the hash of the record before it. Delete one reading and the chain visibly breaks.
Tech Stack
HARDWARE
ESP32-S3 · SHT40 · ethylene sensor · ATECC608B · SX1262 LoRa · PN532 NFC · solar + battery
SOFTWARE
MQTT/TLS · Node.js · MongoDB · Python · TensorFlow Lite · Hyperledger Fabric · GS1 EPCIS
Notes: Trace the orange path with a finger: no signal, keep saving, then only the missing records go up. That branch is the problem statement's own requirement.

## Slide 4
Your Team
Name
FEASIBILITY AND VIABILITY
@SIH Idea submission- Template
4
Aspects of Feasibility
Technical
Every part is a catalogue component
IP67 · −20 to +60 °C · ISTA 3E
36 µA idle · 3.8 year battery
Operational
Switch on and tap — no app to learn
One gateway serves a whole truck
Works with no signal at all
Financial
Node ₹1,839 · gateway ₹3,027
₹140 per shipment, reused 150 times
Made by Indian EMS · PLI eligible
Future Scope & Security
FUTURE
Thermal energy harvesting alongside solar
Shelf-life prediction validated per commodity
SECURITY
Signed in the device — the server cannot forge a reading
Encrypted at rest and in transit · EN 13486 calibration enforced
Potential Challenges, Risks and Mitigation
Challenge
Risk
What We Do
Ethylene sensor not yet chosen
Wrong cost or wrong accuracy
3 options costed — test, then pick
No mobile signal on the route
A gap nobody can explain
Keeps saving; uploads later
LoRa weak inside a steel body
Nodes cannot reach the gateway
Gateway sits at the cargo door
Battery will not charge below 0 °C
Damage on frozen lanes
LiFePO₄, or block charging when frozen
Small firms resist new systems
Nobody adopts it
No app to learn — switch on and tap
Prototype — What We Will Demonstrate
1
The node logging live, sequence numbers on screen
2
Antenna pulled out — it keeps logging, then fills the gap
3
Water sprayed on the sealed box while it keeps running
4
Two nodes disagree → the faulty one is flagged
5
A reading edited in the database → verification fails
COST PER SHIPMENT (₹)
Chart: 
| SecureHarvest | Throw-away USB | Single-use real-time
Cost per shipment | 140 | 499 | 7499
Notes: Say plainly: we costed three ethylene sensors and have not picked one, because we want to test first. Honesty scores here.

## Slide 5
Your Team
Name
IMPACT AND BENEFITS
@SIH Idea submission- Template
5
One Real Trip: Nashik → JNPT
The truck loses signal for 29 hours somewhere past Dhule.
ONLINE
NO SIGNAL — 29 HOURS
BACK ONLINE
up to 1000
1001 … 1350 saved on the device
the gap uploads, in order
WITHOUT AnnaChain
29 hours simply missing. The buyer disputes the load.
0 records recovered
WITH AnnaChain
Every reading kept, then uploaded and checked.
350 records recovered
Shaping Impact
EXPANDED REACH
every crate is watched, not just the truck
FINANCIAL RELIEF
one avoided rejection pays for 780 trips
BETTER OUTCOMES
alerts while the load can still be saved
HEALTHCARE OF FOOD
spoilage caught at the dock and the mandi
ECONOMIC
proof a foreign buyer accepts
SOCIAL
small operators get what only big firms had
Nationwide Impact
81%
of export rejections are paperwork, handling and temperature — not pesticides
80%
of India's cold chain is run by small operators who buy nothing today
5-15%
of fruit and vegetables are lost after harvest
10,000
reefer trucks exist against 62,000 the country needs
Scalability
One gateway already serves a whole truck — adding crates costs ₹1,839 each, not a new subscription
Catalogue parts and Indian EMS: no BGA-only components, no imported assembly
Pilot 20 nodes on one APEDA lane, then FPO clusters under the 10,000-FPO scheme
Records come out as GS1 EPCIS events, so FSSAI and APEDA systems can read them as they are
Works on ordinary LTE where NB-IoT has not reached
Notes: Point at the orange band. Without us those 29 hours are gone and the buyer argues. With us, 350 readings come back in order.

## Slide 6
Your Team
Name
RESEARCH AND REFERENCES
@SIH Idea submission- Template
6
Research and Standards
RESEARCH
NCCD / IIF 2026 — India runs 10,000 reefer trucks against 62,000 needed
IMARC 2025 — cold chain ₹2,536 bn; 80% of capacity unorganised
UNIDO 14-year analysis (Crop Care Federation of India) — 81% of rejections are not pesticide-related
STANDARDS
GS1 EPCIS 2.0 · EN 12830 and EN 13486 · FDA FSMA 204 · EU 178/2002 Art. 18 · MeitY Vishvasya · TEC MTCTE
Insights From Literature
Blockchain alone does not make data true — the reading must be trustworthy before it is written. That is why we sign inside the device.
Cold-chain loggers fail most often at the link, not the sensor. Storing first and reconciling later removes that failure mode.
Ethylene sensing below 1 ppm needs laboratory instruments. We state what we can honestly measure, and cost three options.
Lithium cells cannot be charged below 0 °C without damage — a real trap for frozen lanes, so the design either uses LiFePO₄ or blocks charging when it is that cold.
Every Number, and Where It Came From
WHAT | NUMBER | SOURCE
Reefer trucks India has / needs | 10,000 / 62,000 | NCCD, 2026
Cold chain run by small operators | 80% | IMARC, 2025
Rejections not caused by pesticides | 81% | UNIDO, 14 years
Fruit and vegetables lost after harvest | 5-15% | Lok Sabha, 2024
Throw-away USB logger | ₹499 | market listing
Single-use real-time logger | ₹7,499 | Sensitech, India
Our sensor node | ₹1,839 | our costing
Our shared gateway | ₹3,027 | our costing
Our cost per shipment | ₹140 | our costing
Idle current / battery life | 36 µA / 3.8 yr | our power budget
Full 21-part design document, BOM workbook and reproducible cost and power scripts available on request.